## Slide 1: 2N IP Intercoms Secure, reliable, futureproof

## Slide 2: Why choose IP?
Use of common network infrastructure
Seamless integration with other systems
Advanced features
Easy maintenance and updates
Long-term cost-effectiveness
Investment protection

## Slide 3: IP benefits over 2-wire networks: in detail
Easy integration
IP systems can integrate seamlessly with other devices and systems, such as access control, security cameras, smart homes, and building management systems.
2-wire systems use closed protocols, so they require specialized development for every integration.
Advanced features
IP systems offer a wide range of advanced features, including motion detection, video analytics, cloud storage, automation, and software-based control.
2-wire intercom systems have basic features with minimal potential for adding additional functions.
Use of common infrastructure
IP devices communicate over a local area network (LAN), a common infrastructure found in most homes and businesses.
2-wire systems require dedicated wiring, which limits power, distance and the number of devices.

## Slide 4: IP benefits over 2-wire networks: in detail
Long-term cost-effectiveness
Fewer cables and maintenance requirements, plus easier upgrades = lower overall costs, despite the more expensive installation.
2-wire systems may be cheaper initially, but wiring and hardware limitations mean that upgrading the system can increase costs.
Investment protection
Unlike 2-wire systems, IP continues to deliver.
With continuous new firmware releases, IP systems offer a future-proof solution.
Projects can get enhanced new features and security patches, without additional costs.
Easy maintenance and updates
IP-based systems can be remotely maintained, updated and configured, reducing the need for on-site maintenance.
2-wire systems require physical access to the system, making it more time-consuming and costly.

## Slide 5: Why choose 2N?
Your building deserves high-quality door control
Choose from a range of IP intercoms from an industry leader that prioritizes reliability and innovation

## Slide 6
Integrate without limits
Get multifunctional devices
Meet the needs of any project
We build our devices on open protocols, partner with over 200 leading brands, and make easy integration a priority
Combine audio, video, and a reader in a single device that also supports several access methods
You need flexibility, and we have a wide range of flexible devices that suit every vertical

## Slide 7
Rely on true innovators
For new builds & retrofits
Prioritize cybersecurity
Collaborate with the company that launched the world’s first IP intercom – and that’s kept innovating ever since
Advanced intercoms that are the perfect fit for modern newbuilds – but also work in retrofit projects with tricky cabling requirements.
An ISO 27001-certified company, cybersecurity is our priority. We design intercoms based on proven security models such as Axis' ASDM

## Slide 8
European quality
5-year warranty
No need for SIP servers
Designed and manufactured in Europe using high-quality components, with strong reliability in mind
Our intercoms are Built to Last. The 5-year warranty, standard on all hardware, reflects our commitment to high-quality, reliable tech
2N IP intercoms work as standalone devices and support direct SIP calls

## Slide 9: Meet new cybersecurity requirements
Secure boot: SW authenticity verified by HW from 2N production
Secure storage: All data encrypted (config, directory, certificates)
Signed firmware: Only 2N-signed OS accepted
Password policy: Forced change during setup
No extra interfaces: Production interfaces disabled post-setup
Secure communication: HTTPS, SIPS, SRTP, TLS 1.2, 112+ bit keys
No known vulnerabilities: Aligned with 2N R&D and vulnerability policies

## Slide 10: Ensuring access & motion. For all.
Compliant with the European Accessibility Act
High-quality audio & visuals over VoIP
Create an accessible intercom screen with our custom GUI builder on the 2N IP Style
Pictograms: intercom state signals that guide deaf users
Induction loops for users of hearing aids
Audio prompts & navigation for blind & visually impaired users
Adaptive face-zooming ensures visibility of wheelchair users in a wide-angle shots

## Slide 11: Intercoms that secure any entrance
Single-family homes
Industrial sites
Healthcare & education
Apartment buildings
Offices & mixed-use buildings
Hospitality
Notes: More in-depth?

## Slide 12: Intercoms ready for easy integration
www.2n.com
SIP
RTSP/RTP
HTTP API
Plugins
ONVIF
Wiegand
RIO
Notes: * Old graphic

## Slide 13: The 2N portfolio

## Slide 14: 2N IP Style
Defining future standards for video intercoms
Notes: RED Badge?

## Slide 16: 2N IP Style features
The camera of the future
Enhance your projects with an intercom that can handle multiple simultaneous Full HD streams and has a 5 MPx chip.
It supports WDR and provides clear colour images, even in low-light conditions.
Adaptive Face Zooming enhances the wide-angle lens for crystal clear visitor verification.

## Slide 17: 2N IP Style features
A customisable display
2N Flexi Layout allows you to craft a completely custom intercom screen to meet the needs of any customer.
Create personalized homepages, display videos, add custom buttons with useful required actions, and more.

## Slide 18: 2N IP Style features
Premium 10“ display
The extreme brightness of the display guarantees excellent readability, even in direct sunlight.
IP65 and IK08 durability
The 2N IP Style can easily resist heavy rain, a dusty environment, and even attacks by vandals.
Modern, versatile access
Offer smooth, secure, and reliable access to buildings. Choose from mobile access, QR codes, PIN, and RFID – all in one device
Notes: Order numbers - sitelink

## Slide 19: 2N IP Verso 2.0
Create an intercom for any project imaginable

## Slide 21: 2N IP Verso 2.0 features
Advanced Modularity
Combine 16 different modules and 4 installation options to create the ideal intercom for your project.
Choose any Access Control Option
RFID readers, keypads, fingerprint readers, Bluetooth readers and/or a combination of them all.
Wide-Angle Full HD Camera
It provides crystal-clear colour images, supports WDR, and maintains image colour even in low light conditions.

## Slide 22: 2N IP Force 2.0
The world’s most durable IP intercom with a 5MPX camera

## Slide 23: 2N IP Force 2.0 features
Our most durable unit
An extremely durable intercom made from aluminium, it will withstand extreme conditions, including dust, water, and significant impact.
It also has a dome over the camera for greater shatter resistance.
Notes: Material – the same, the chassis is slightly different. On the front panel, we removed the plastic side panels – nothing to break to get inside, harder to get into, no weak point!
The frame – might be easily removed. Only for flush installations, to avoid this issue, it can be installed surface or on a gooseneck.
Dome – the same dome that Axis uses on their mini-cameras, highly resistant

## Slide 24: 5MPx camera
Ensures clear colour images even in low light, switching to night vision only in complete darkness.
It also supports WDR to prevent glare, and the wide-angle lens is enhanced with adaptive face zooming for excellent visitor verification.
Notes: Key improvement from the last generation – the camera. As is standard with ARTPEC devices, this camera is very high quality – more than HD images – QHD. It offers all the features you’d expect for reliable visitor verifiction – night vision, WDR, and adaptive face zooming.

## Slide 25: 2N IP Force 2.0 features
Clear, reliable sound
Noise cancellation, a high-volume speaker, adaptive volume, and automatic audio-loop tests all ensure effective communication you can count on in loud, busy environments.
Robust access control
Choose from RFID, keypad, or button units.
OSDP support also enables encrypted RFID access and communication with third-party access control systems
QR code access
The Axis ARTPEC-8 powers multiple advanced features, including QR code reading.
Use it to assign guests QR code access in advance to ensure seamless guest entry.

## Slide 26: 2N IP Safety
Designed for emergency communications
Reliable communication
IK10 & IP69K certified
Always visible and functional
Integrates into existing systems
Choose from three versions: one button, two buttons, or a raised emergency button.

## Slide 27: 2N IP One
One Family. One Home. One Smart Intercom.

## Slide 29: 2N IP One features
Great durability
This is no ordinary plastic video doorbell.
With IP66 & IK08 certifications, the 2N IP One is truly durable.
The body is made of high-quality anodized aluminum, which ensures exceptional resistance to vandals, water, and dust.

## Slide 30: 2N IP One features
Full HD surveillance
Enhance home security with motion detection. Residents will be notified, and the Full HD camera will record the surroundings immediately
Easy integration
Based on open protocols and supporting multiple plug-ins, you can integrate the intercom easily with leading third-party technology
.
Door control
Connect the door strike to the 2N IP One so that residents can answer the door via the My2N app/indoor station, let visitors in with QR codes, or unlock the door using the app.

## Slide 31: 2N IP Solo
A great addition to smart home entrances
Hidden HD camera
Compact design
Integrates with home automation
Available in nickel and black

## Slide 32: 2N IP Base
Designed especially for smaller-scale installations
Compact IP intercom with HD camera
High-quality video & audio
Very easy to install

## Slide 33: 2N IP Uni
For general-purpose outdoor and indoor environments
Dependable communication with emergency services or helpdesks
Easy installation
Visual status signalling
Effectively replaces analogue intercoms

## Slide 34: 2N IP Audio Kit
OEM intercom intended for incorporation into a variety of devices
Adds value to both audio communication and remote surveillance and control
A VoIP solution you don’t have to develop
Remote configuration
A wide range of connectors

## Slide 35: Key takeaways: Why choose 2N IP intercoms
Innovation
Seamless access
Versatility: an intercom for any vertical
Easy integration
Built to last in the EU
Strong cybersecurity
Easy remote setup and management
Core part of a 2N access solution
EU
Notes: RED-compliant

## Slide 36: Offer your customers the best in modern intercoms